## Slide 1: Take Our Kids to Work - Oakville

## Slide 2: Soybeans and Canola Seeds Arrive in Hamilton

## Slide 3
Bean Cleaning
Cooking
Cracking
Meal
SOYBEAN EXTRACTION
(soybean ~ 18% oil)
Flaking
Extraction
Hulls
Extracted Oil
Degumming
Dehulling
Notes: Bean Cleaning: Removes pods, stalks, stones, etc.
Cooking: Beans are heated to inactivate enzymes that are naturally present. Otherwise oil damage would occur. Heating also facilitates hull removal.
Cracking: Beans are cracked into 4 to 6 pieces. Hulls are now loose.
Dehulling: Hulls are removed by aspiration. They contain large amounts of fiber. Hull removal improves meal quality. Hulls are sold as a by-product.
Flaking: Bean pieces pass through rollers making a flake (like a corn flake). Oil bearing cells are opened.
Extraction: Oil removed by solvent extraction using hexane.
Meal: Soybean meal containing ~45% protein is sold for animal feed formulations.
Degumming: Oil is mixed with a small amount of water and centrifuged to remove phosphorus compounds (lecithin).

## Slide 4
Seed Cleaning
Flaking
Cooking
Meal
CANOLA SEED EXTRACTION
(canola seed ~ 42% oil)
Pressing
Extraction
Press Oil
Extracted Oil
Degumming
Notes: Seed Cleaning: Removes pods, stalks, stones, etc.
Flaking: Seed passes through rollers making a small flake. Oil bearing cells are opened.
Cooking: Flakes are heated to inactivate enzymes that are naturally present. Otherwise oil damage would occur. Heating also reduces oil viscosity making pressing easier.
Pressing: ~55% of the oil is squeezed from cooked flakes in high pressure screw press.
Extraction: Balance of oil is solvent extracted using hexane.
Meal: Canola meal containing ~35% protein is sold for animal feed formulations.
Degumming: Press and extracted oils are combined. Oil is mixed with a small amount of water/acid and centrifuged to remove phosphorus compounds.

## Slide 5
Degummed Oil
Alkali Refining
Bleaching
Deodorization
Hydrogenation
Blending
Other Oils
OIL PROCESSING
Notes: Alkali Refining: Oil is mixed with acid and dilute caustic soda. Centrifugation removes free fatty acids, phosphorus compounds, and trace metals.
Bleaching: Oil is contacted with bleaching earth and subsequently filtered. Bleaching removes colour pigments, chlorophyll (especially in canola oil) and trace metals.
For salad/cooking oil production, bleached oil goes straight to deodorization.
Deodorization: Oil is subjected to high temperature under very low vacuum. This drives off volatile compounds that contribute to odour and flavour. A bland product is produced.
For shortening production, the bleached oil goes to hydrogenation.
Hydrogenation: Oil is combined with hydrogen gas under high pressure/high temperature in the presence of a nickel catalyst. This increases the melting point of the fat and increases oxidative stability.
Blending: Depending on the required product, various hydrogenated fats are blended to meet specifications.

## Slide 6: Soybeans and Canola Seeds are Processed in Hamilton

## Slide 7: Arrives in Oakville
Refined, Bleached, Deodorized oil arrives in Oakville

## Slide 8: Leaves Oakville
Packaged Product leaves Oakville

## Slide 9: Leaves Oakville
Packaged Product leaves Oakville

## Slide 10: Liquid Oils
Types
Canola
Soybean
High Oleic Canola Oil
  Nutra Clear
  Buttery Griddle Oil
  Popcorn Popping Oil
Mid Oleic Sunflower Oil

## Slide 11: Liquid Oils
Package Formats – 3 & 5L Bottle

## Slide 12: Liquid Oils
Package Formats – 16L JIB

## Slide 13: Liquid Oils
Package Formats – 16 L BIB

## Slide 14: Liquid Oils
Package Formats – 900 kg NR Tote

## Slide 15: Liquid Oils
Applications
Salad Dressing
Baking (eg Bread, Muffins)
Griddle and Popcorn Popping
Deep Frying

## Slide 16: Solid Shortening
Types
Hydrogenated
  Soybean, canola, cottonseed and palm blends
Non Hydrogenated
  Soybean, canola, palm and palm kernel blends
Animal Fats
  Lard, tallow

## Slide 17: Solid Shortening Crystallizer
Change in State from liquid to solid

## Slide 18: Solid Shortening
Crystallization Equipment – Cooling Barrel

## Slide 19: Solid Shortening
Crystallization Equipment - Pinworker

## Slide 20: Solid Shortening
Slow Cooling Rate
Fast Cooling Rate
Fewer and larger crystals
↓ Surface area
↓ SFC
↓ Hardness
Many and smaller crystals
↑ Surface area
↑ SFC
↑ Hardness
Cooling Rate and Crystallization

## Slide 21: Solid Shortening
Package Formats
1 # prints, 2.5 # tubs, 3# tubs
  Shortening
  Lard
20 kg and 50#
  Hydrogenated vegetable
  Non hydrogenated vegetable
  Lard
  Tallow

## Slide 22: Solid Shortening
Package Formats – Retail Line

## Slide 23: Solid Shortening
Package Formats – Cube Line

## Slide 24
OXIDATIVE
STABILITY
NUTRITION
FUNCTIONALITY
The
Dream Fat
Solid Shortening
Selecting a Type of Solid Shortening

## Slide 25: Solid Shortening Determine your Objectives: Functionality
Although fats and oils share a common molecular structure…
…they fulfill different functions in a given formula or application

## Slide 26: Solid Shortening General Purpose, Emulsified, Laminating, Frying

## Slide 27: Solid Shortening General Purpose Shortenings in Cookies

## Slide 28: Solid Shortening Effects of Various Fats in Lamination

## Slide 29: Margarine
Spreading
Sauteeing
Baking
Icing
Laminating

## Slide 30: Whip Toppings
Non-dairy
Lactose free
Liquid, not frozen
No thawing, ready to whip
Stable foam